CAN Data Logger
---------------------------------------------

Implementation 1 : Basic CAN protocol implementation
--------------------------------------------------------------------
Controller : ESP32
Transceiver : SN65HVD230 CAN Board Network Transceiver Evaluation Development Module
Device Spec
----------------

        ESP32
Processors: CPU: Xtensa dual-core (or single-core) 32-bit LX6 microprocessor, operating at 160 or 240 MHz and performing at up to 600 DMIPS
Ultra low power (ULP) co-processor
- Memory: 320 KiB RAM, 448 KiB ROM
- Wireless connectivity:
  - Wi-Fi: 802.11 b/g/n
  - Bluetooth: v4.2 BR/EDR and BLE (shares the radio with Wi-Fi)
- Peripheral interfaces:
  - 34 × programmable GPIOs
  - 12-bit SAR ADC up to 18 channels
  - 2 × 8-bit DACs
  - 10 × touch sensors (capacitive sensing GPIOs)
  - 4 × SPI
  - 2 × I²S interfaces
  - 2 × I²C interfaces
  - 3 × UART
  - SD/SDIO/CE-ATA/MMC/eMMC host controller
  - SDIO/SPI slave controller
  - Ethernet MAC interface with dedicated DMA and planned IEEE 1588 Precision Time Protocol support[4]
  - CAN bus 2.0
  - Infrared remote controller (TX/RX, up to 8 channels)
  - Motor PWM
  - LED PWM (up to 16 channels)
  - Hall effect sensor
  - Ultra low power analog pre-amplifier
- Security:
  - IEEE 802.11 standard security features all supported, including WPA, WPA2, WPA3 (depending on version)[5] and WAPI
  - Secure boot
  - Flash encryption
  - 1024-bit OTP, up to 768-bit for customers
  - Cryptographic hardware acceleration: AES, SHA-2, RSA, elliptic curve cryptography (ECC), random number generator (RNG)
- Power management:
  - Internal low-dropout regulator
  - Individual power domain for RTC
  - 5 μA deep sleep current
  - Wake up from GPIO interrupt, timer, ADC measurements, capacitive touch sensor interrupt

SN65HVD230 CAN transceiver
1. Powered from 3.3V
2. Features ESD protection
3. Connecting MCUs to the CAN network
4. Compatible with PCA82C250

CAN Bus Implementation
---------------------------------------------
CANH - > 2.5V to 3.3V
CANL -> 0v to 2.5V

120E resister between CANH and CANL

Reference
---------------------------------------------
https://hackaday.com/2017/01/04/on-board-diagnostics/
http://www.obddiag.net/allpro.html
https://www.hackster.io/news/the-can32-an-esp32-based-can-bus-board-af5c9e1bd8ec

[CAN Bus Library]

https://www.arduino.cc/reference/en/libraries/can/
https://github.com/sandeepmistry/arduino-CAN

[ESP32]

https://www.google.com/url?sa=t&rct=j&q=&esrc=s&source=web&cd=&ved=2ahUKEwiAmom9yZL1AhVLzjgGHQz4DrgQFnoECBIQAQ&url=https%3A%2F%2Fwww.espressif.com%2Fsites%2Fdefault%2Ffiles%2Fdocumentation%2Fesp32_datasheet_en.pdf&usg=AOvVaw0aPqs26KTwgQAQ33yEvdPB

https://www.electronicshub.org/getting-started-with-esp32/

https://randomnerdtutorials.com/esp32-dual-core-arduino-ide/

[CAN Bus USB ]
https://www.youtube.com/watch?v=kkdRdKbMhPI